## Slide 1: Example: 1) Statement of problem to be solved
  Marketing statement:
    I want to focus (and scan) a laser beam on a sample inside a vacuum chamber. Size of the chamber is 80mm in diameter.
  Technical statement:
    Focal length of 40mm is required, i.e. from requirements for scanning speed.
    Wavelength:
    Spot size:
    f’=40mm.
    Working distance (=fb) > 45mm.
    Less number of elements is desirable for alignment.
    Anything else?
80mm
Optical
System
Laser
Sample
Chamber
45mm
Scanning
mirror

## Slide 2: 2) Alternative designs 3) First order designs: geometrical design of optics
Single thin lens
f’=40mm
Thick lens
(01LDX313,f=40mm)
H
H’
f’=40
fb=39
Two thin element system
f’sys=40, fb = 80
f’=-40
f’=+40
40
Ray matrix
Graphical ray tracing
40
40
n
Thick lens
01LDX313
f=40mm
Thick lens
01LDK117
f=-40mm
F’sys
F’sys
F’sys
40 n
79
80
H H’
H H’
Single thick lens
Single thick lens
Two thick lenses
Start!
F’sys
F’sys
f’=40

## Slide 3: 4) Evaluate against objectives 5) Select most promising solution (1st order. solution)
H
H’
f’=40
fb=39
40
n
F’sys
F’sys
40 n
79
80
H H’
H H’
1) Single thick lens
2) Single thick lens
3) Two thick lenses
F’sys
 | 1) Single thick lens | 2) Single thick lens | 3) Two thick lenses
1. l=532nm | 532 | 532 | 532
2. f’sys =40mm | 40 | 40 | 40
3. fb>45mm | 39 (< 45) | 80 | 79
4. # of elements | 1 | 1 | 2
5. Spot size<10mm | 2.44l(F/#)=4.15mm, (F/#)=3.2 | Need further evaluation by ray tracing (Step 6 and thereafter.) Note: too thick! (~60mm) | 2.44l(F/#)=8.3mm, (F/#)=6.4 Need further evaluation by ray tracing (Step 6 and thereafter.)