## Slide 1
Introduction to Optical Design Yuzuru Takashima, Ph.D.
Associate Professor College of Optical Sciences University of Arizona 1630 E. University Blvd. Tucson, AZ 85721 ytakashima@optics.arizona.edu www.optics.arizona.edu

## Slide 2: Introduction to Optical Design Lecture #1
Yuzuru Takashima
College of Optical Sciences
ytakashima@optics.arizona.edu

## Slide 3
Design Procedure
  How to design lens system?
    Exercise 1: Use catalog lens in CodeV
Review of 1st order optics
  Why 1st order ? How 1st order optics are related to 3rd order aberrations?
Ray-trace

## Slide 4
1. Statement of problem to be solved:
Objective
Marketing and Technical statement
5. Select most promising solution(s)
(1st order solution)
2. Alternative designs:
Several options for solving the stated problem/objective
3. First order designs:
8. Carry out ray tracing design of most promising 1st order design
9. Carry out tolerance analysis, manufacturing and cost analysis
4. Evaluate
against objectives
7. Evaluate
against objectives
10. Evaluate
against objectives
Yes
No
Yes
No
6. Carry out 3rd order analysis
(3rd order solution)
1) Statement of problem to be solved:
  Objective
  Technical statement (PRD: Product Requirement Document)
  Marketing statement (MRD: Marketing Requirement Document), which translates into a technical statement
2) Alternative designs:
  Several options for solving the stated problem/objective
3) First order designs: geometrical design of optics
4) Evaluate against objectives
5) Select the most promising solution(s) (1st order. solution)
6) Carry out ray tracing design of most promising first order design
7) Evaluate design against objectives; optimize against “cost” factor
8) Go through loop 6, 7, 6, 7 until satisfactory results emerge, or 3, 4, 5, 6, 7
9) Carry out tolerance analysis, manufacturing and cost analysis, repeat 3-8 if necessary
10) Write report
Design Procedure

## Slide 5: Waterfall v.s. Agile Process
Waterfall process
  Mainly used for a hardware design.
  It is very important to follow the process!
    A self-reviewing process
    Logical development
    Easy to recover errors

## Slide 6: Agile Process
Agile Process
  For software development, it is generally difficult to define PRD completely.
    Look & Feel
    User experience.
Specification
MRD
PRD
Testing

## Slide 7: Example: 1) Statement of problem to be solved
  Marketing statement:
    I want to focus (and scan) a laser beam on a sample inside a vacuum chamber. Size of the chamber is 80mm in diameter.
  Technical statement:
    Focal length of 40mm is required, i.e. from requirements for scanning speed.
    Wavelength:
    Spot size:
    f’=40mm.
    Working distance (=fb) > 45mm.
    Less number of elements is desirable for alignment.
    Anything else?
80mm
Optical
System
Laser
Sample
Chamber
45mm
Scanning
mirror

## Slide 8: 2) Alternative designs 3) First order designs: geometrical design of optics
Single thick lens
Single thick lens
Two thick lenses
Single thin lens
f’=40mm
Thick lens
(01LDX313,f=40mm)
H
H’
f’=40
fb=39
Two thin element system
f’sys=40, fb = 80
f’=-40
f’=+40
40
Ray matrix
Graphical ray tracing
40
40
n
Thick lens
01LDX313
f=40mm
Thick lens
01LDK117
f=-40mm
F’sys
F’sys
F’sys
40 n
79
80
H H’
H H’
Start!
F’sys
F’sys
f’=40

## Slide 9: 4) Evaluate against objectives 5) Select most promising solution (1st order. solution)
H
H’
f’=40
fb=39
40
n
F’sys
F’sys
40 n
79
80
H H’
H H’
1) Single thick lens
2) Single thick lens
3) Two thick lenses
F’sys
 | 1) Single thick lens | 2) Single thick lens | 3) Two thick lenses
1. l=532nm | 532 | 532 | 532
2. f’sys =40mm | 40 | 40 | 40
3. fb>45mm | 39 (< 45) | 80 | 79
4. # of elements | 1 | 1 | 2
5. Spot size<10mm | 2.44l(F/#)=4.15mm, (F/#)=3.2 | Need further evaluation by ray tracing (Step 6 and thereafter.) Note: too thick! (~60mm) | 2.44l(F/#)=8.3mm, (F/#)=6.4 Need further evaluation by ray tracing (Step 6 and thereafter.)

## Slide 10: Law of geometrical optics
1) Rays propagate along straight line in a homogeneous and isotropic medium.
2) Light is refracted from the boundary between two media having different propagation speeds, or indices of refraction (n=Co/C, Co: speed of light in vacuum). The incoming ray, the refracted ray, and the surface normal lie in a plane.
  Snell’s Law (Law of refraction)
3) Upon reflection, the incoming, reflected ray and the surface normal lie in a plane.
  Law of reflection

## Slide 11: Law of geometrical optics
Besides the three law of geometrical optics, there are extremely important principles, which can be derived from the law of geometrical optics and vise versa
  Huygens’ Principle (1690)
  Fermat’s Principle (1650)
  Eikonal Equation (1911)

## Slide 12: Huygens’ Principle (1690)
Each element of a wavefront may be regarded as the center of a secondary disturbance which gives rise to spherical wavelets. The position of the wavefront at any later time is the envelope of all such wavelets. (Assume wavelets propagates in the direction of ray)

## Slide 13: Fermat’s Principle (1650)
A light ray always forms a trajectory that makes the optical path length (OPL) a stationary value: in general a minimum, sometimes a maximum.

## Slide 14: Eikonal Equation (1911)
The square of the gradient of the Ekonal* is equal to the index of refraction squared.

## Slide 15: Jell-O Gradient Index Lens

## Slide 16
Fabrication Recipe

## Slide 17: GRIN lens
Light wave
n: Index of refraction ~ 1.5
Light wave
n ~ 1.5
Velocity in glass = c/n

## Slide 18: Two types of compound eyes
http://www.nature.com/nature/journal/v287/n5784/pdf/287681a0.pdf
Apposition Eyes
2) Superposition Eyes
(nocturnal insects, crustaceans)

## Slide 19: Modeling of Compound Eyes Apposition and Superposition Eyes
GrinSingleFocus.seq
GrinUnitTele.seq
Apposition Eyes
2) Superposition Eyes

## Slide 20: Review: 1st order optics