## Slide 1
Introduction to Optical Design Yuzuru Takashima, Ph.D.
Associate Professor College of Optical Sciences University of Arizona 1630 E. University Blvd. Tucson, AZ 85721 ytakashima@optics.arizona.edu www.optics.arizona.edu

## Slide 2: Introduction to Optical Design Lecture #1
Yuzuru Takashima
College of Optical Sciences
ytakashima@optics.arizona.edu

## Slide 3
Design Procedure
  How to design lens system?
    Exercise 1: Use catalog lens in CodeV
Review of 1st order optics
  Why 1st order ? How 1st order optics are related to 3rd order aberrations?
Ray-trace

## Slide 4
1. Statement of problem to be solved:
Objective
Marketing and Technical statement
5. Select most promising solution(s)
(1st order solution)
2. Alternative designs:
Several options for solving the stated problem/objective
3. First order designs:
8. Carry out ray tracing design of most promising 1st order design
9. Carry out tolerance analysis, manufacturing and cost analysis
4. Evaluate
against objectives
7. Evaluate
against objectives
10. Evaluate
against objectives
Yes
No
Yes
No
6. Carry out 3rd order analysis
(3rd order solution)
1) Statement of problem to be solved:
  Objective
  Technical statement (PRD: Product Requirement Document)
  Marketing statement (MRD: Marketing Requirement Document), which translates into a technical statement
2) Alternative designs:
  Several options for solving the stated problem/objective
3) First order designs: geometrical design of optics
4) Evaluate against objectives
5) Select the most promising solution(s) (1st order. solution)
6) Carry out ray tracing design of most promising first order design
7) Evaluate design against objectives; optimize against “cost” factor
8) Go through loop 6, 7, 6, 7 until satisfactory results emerge, or 3, 4, 5, 6, 7
9) Carry out tolerance analysis, manufacturing and cost analysis, repeat 3-8 if necessary
10) Write report
Design Procedure

## Slide 5: Waterfall v.s. Agile Process
Waterfall process
  Mainly used for a hardware design.
  It is very important to follow the process!
    A self-reviewing process
    Logical development
    Easy to recover errors

## Slide 6: Agile Process
Agile Process
  For software development, it is generally difficult to define PRD completely.
    Look & Feel
    User experience.
Specification
MRD
PRD
Testing

## Slide 7: Example: 1) Statement of problem to be solved
  Marketing statement:
    I want to focus (and scan) a laser beam on a sample inside a vacuum chamber. Size of the chamber is 80mm in diameter.
  Technical statement:
    Focal length of 40mm is required, i.e. from requirements for scanning speed.
    Wavelength:
    Spot size:
    f’=40mm.
    Working distance (=fb) > 45mm.
    Less number of elements is desirable for alignment.
    Anything else?
80mm
Optical
System
Laser
Sample
Chamber
45mm
Scanning
mirror

## Slide 8: 2) Alternative designs 3) First order designs: geometrical design of optics
Single thick lens
Single thick lens
Two thick lenses
Single thin lens
f’=40mm
Thick lens
(01LDX313,f=40mm)
H
H’
f’=40
fb=39
Two thin element system
f’sys=40, fb = 80
f’=-40
f’=+40
40
Ray matrix
Graphical ray tracing
40
40
n
Thick lens
01LDX313
f=40mm
Thick lens
01LDK117
f=-40mm
F’sys
F’sys
F’sys
40 n
79
80
H H’
H H’
Start!
F’sys
F’sys
f’=40

## Slide 9: 4) Evaluate against objectives 5) Select most promising solution (1st order. solution)
H
H’
f’=40
fb=39
40
n
F’sys
F’sys
40 n
79
80
H H’
H H’
1) Single thick lens
2) Single thick lens
3) Two thick lenses
F’sys
 | 1) Single thick lens | 2) Single thick lens | 3) Two thick lenses
1. l=532nm | 532 | 532 | 532
2. f’sys =40mm | 40 | 40 | 40
3. fb>45mm | 39 (< 45) | 80 | 79
4. # of elements | 1 | 1 | 2
5. Spot size<10mm | 2.44l(F/#)=4.15mm, (F/#)=3.2 | Need further evaluation by ray tracing (Step 6 and thereafter.) Note: too thick! (~60mm) | 2.44l(F/#)=8.3mm, (F/#)=6.4 Need further evaluation by ray tracing (Step 6 and thereafter.)

## Slide 10: Law of geometrical optics
1) Rays propagate along straight line in a homogeneous and isotropic medium.
2) Light is refracted from the boundary between two media having different propagation speeds, or indices of refraction (n=Co/C, Co: speed of light in vacuum). The incoming ray, the refracted ray, and the surface normal lie in a plane.
  Snell’s Law (Law of refraction)
3) Upon reflection, the incoming, reflected ray and the surface normal lie in a plane.
  Law of reflection

## Slide 11: Law of geometrical optics
Besides the three law of geometrical optics, there are extremely important principles, which can be derived from the law of geometrical optics and vise versa
  Huygens’ Principle (1690)
  Fermat’s Principle (1650)
  Eikonal Equation (1911)

## Slide 12: Huygens’ Principle (1690)
Each element of a wavefront may be regarded as the center of a secondary disturbance which gives rise to spherical wavelets. The position of the wavefront at any later time is the envelope of all such wavelets. (Assume wavelets propagates in the direction of ray)

## Slide 13: Fermat’s Principle (1650)
A light ray always forms a trajectory that makes the optical path length (OPL) a stationary value: in general a minimum, sometimes a maximum.

## Slide 14: Eikonal Equation (1911)
The square of the gradient of the Ekonal* is equal to the index of refraction squared.

## Slide 15: Jell-O Gradient Index Lens

## Slide 16
Fabrication Recipe

## Slide 17: GRIN lens
Light wave
n: Index of refraction ~ 1.5
Light wave
n ~ 1.5
Velocity in glass = c/n

## Slide 18: Two types of compound eyes
http://www.nature.com/nature/journal/v287/n5784/pdf/287681a0.pdf
Apposition Eyes
2) Superposition Eyes
(nocturnal insects, crustaceans)

## Slide 19: Modeling of Compound Eyes Apposition and Superposition Eyes
GrinSingleFocus.seq
GrinUnitTele.seq
Apposition Eyes
2) Superposition Eyes

## Slide 20: Review: 1st order optics

## Slide 21: Geometrical Theory of Optical System
Optical Axis (z)
Left-hand space
(un-dashed qty)
Right-hand space
(dashed qty)
(+)
(-)
Distance
Propagation direction
A single refractive surface divides the space
in two half spaces.

## Slide 22: Geometrical Theory of Optical System
Conjugate quantities
  The image is conjugate to the object.
  Refracted ray is conjugate to the incident ray
  The plane through the object and image are conjugate planes

## Slide 23: Geometrical Theory of Optical System
An optical system can be completely described by its cardinal planes.
  Two focal planes (F.P.)
  Two principal planes (P.P.)
  Two nodal points (N.P.)

## Slide 24: Cardinal points
1st P.P.
2nd P.P.
n
n’
2nd F.P.
1st F.P.
f’
x’
f
x
z
l’
l

## Slide 25: Cardinal points/planes
First focal plane:
  The first focal plane on the plane in the left-hand space that is perpendicular to the axis and is conjugate to a similar plane at Infinity in the right-hand space.
Second focal plane:
  Left-hand -> Right-hand
  Infinity -> -Infinity

## Slide 26: Cardinal points/planes
Principal Planes
  The principal planes are two conjugate planes for which the lateral magnification is unity.
Nodal Points
  The Nodal points are two conjugate points for which the angular magnification is unity.

## Slide 27: Sign Conventions
Optical Axis (z)
(+)
(-)
Distance
Propagation direction
R1
R2
R1>0
R2<0
t (>0)
C1
C2
Left-hand space: LHS
Right-hand space: RHS
Angle (-)
Angle (+)

## Slide 28: Sign Conventions
Ray travels from left to right
Object is in LHS space, image in at RHS space of lens system.
Radius “R” has a sign.
  “C” center of radius of curvature
    “C” is in RHS with respect to the surface, R>0.
    “C” is in LHS with respect to the surface, R<0.
Distance, “t” (or “d”) has a sign

## Slide 29: Sign Conventions
Distance, “t” (or “d”) has a sign
  See the example
Angles: angles are measured from reference.
  CCW: Positive
  CW: Negative
Remember: The conventions is applicable when you use CodeV.

## Slide 30: Graphical Ray Trace
F1’
Lens 1
Lens 2
F1
F2
F2’

## Slide 31: Graphical Ray Trace
Lens 1 (-f)
Lens 2 (+f)
f

## Slide 32: Ray Matrices
Question: How can we calculate the location of the principal planes with respect to the system components?
I: Input Plane
II: Output Plane
Height: x1
Angle: x1’ = 0
t2
f’sys
s2
Ray
F’
P’

## Slide 33: Ray Matrices
Assumptions
  Paraxial approximation: sin(theta) ~ theta
  Rays are described by angle(y’) and height (y)
Problem to be solved.
  Given ,at the input plane (I)
  calculate at the output plane (II)
  Them use the table to locate cardinal points with respect to the planes I or II.

## Slide 34: Ray Matrices
Plane 1
Plane 2
Height: y1
Angle: y1’
Ray
P’
Height: y2
Angle: y2’
y1
y2
Lens surfaces

## Slide 35: Ray Matrices
Question: How can we calculate the location of the principal planes with respect to the system components?
I: Input Plane
II: Output Plane
Height: x1
Angle: x1’ = 0
t2
f’sys
s2
Ray
F’
P’
Ay1
Cy1

## Slide 36: Ray Matrices
I: Input Plane
II: Output Plane
Height: y1
Angle: y1’ = 0
t2
f’sys
s2
Ray
F’
P’
Ay1
Cy1

## Slide 37: Cardinal Points

## Slide 38: Components of System Matrix: Msys 1. Free space propagation
Optical Axis (z)
y1
y2
y’1
y’2
l

## Slide 39: Components of System Matrix 2. Refraction at curved interface
Incoming ray
Refracted ray
a (<0)
y2’
y1’
q2
q1
q2
n
n’
y1=y2
R=Inf
Curved interface
Planar interface

## Slide 40: 1: Thin lens
F N P I II P’ N’ F’

## Slide 41: 2: System of two thin lenses
I
II

## Slide 42: 3: Thick Lens
I
II

## Slide 43: Imaging Condition
Optical Axis (z)
I
II
y’I
y’II
yI
yII

## Slide 44: Design Project #1
Implement the 1st order design by using off-the-shelf lens (catalog lens) in CodeV
File to be used
  DP1BlankLens.seq
  search.seq (CodeV macro)
Lens drawing commands
“pim”: Paraxial image solve.
“del pim”: Delete pim
“vie;go”: Draw the lens
“lis”: List first order quantities.
“wrl MySinglet”: Save lens as MySinglet.seq (text format, editable)
“in MySinglet”: Load the lens file, MySinglet.seq

## Slide 45: Example: Bi-concave thick lens Melles Griot 01LDK117

## Slide 46: Example: Bi-convex thick lens Melles Griot 01LDX313

## Slide 47: CodeV Lens Database
Copy C:\CODEV104\macro\search.seq in the working directory, C:\CVUSER104\
In the command window, type “in search”
“pim”: Paraxial image solve.
“del pim”: Delete pim
“vie;go”: Draw the lens
“lis”: List first order quantities.
“wrl MySinglet”: Save lens as MySinglet.seq (text format, editable)
“in MySinglet”: Load the lens file, MySinglet.seq

## Slide 48: Introduction to Optical Design Lecture #2
Yuzuru Takashima
College of Optical Sciences
ytakashima@optics.arizona.edu

## Slide 49: Aberration of the rotationally symmetric Optical System
Paraxial systems are perfect in terms of,
  A point is imaged to a point.
  Lateral magnification has no ray height/angle dependence.
    Remember the matrix component “A” has no y, y’ dependence.
Aberrations describe the deviation of real systems from the perfection.
  Paraxial image is used as a reference to measure aberrations.

## Slide 50: Aberration of the rotationally Symmetric Optical System
An aberrated system will have image locations and magnifications approximately the same as those predicted by the paraxial analysis.
Aberrations result from the breakdown of the paraxial assumptions.

## Slide 51: Aberration of the rotationally Symmetric Optical System
The breakdown of the paraxial assumptions.
  Real angles must be used. Not paraxial angles.
    This removes linearity of ray traces. Real rays do not scale.
  Surface sag have to be considered.
    Refraction occurs at the surface of the sphere, not at its vertex plane.
  Ray rays may leave the meridional (y-z) plane.: Skew Rays.
These aberrations exist for perfectly manufactures systems.(Remember the demo of the exact ray trace.)
  Spherical surfaces are true spheres, and there are no-tilted or de-centered elements.

## Slide 52: Expansion of Sin(i) in Snell’s Law
Third order contributions
Paraxial
approximation

## Slide 53: Coordinate System
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h
h: Object height
A ray is specified by object height and pupil coordinate.
The angle q is measured
from the yp axis
Paraxial
Image
Ray aberration measured
from the paraxial image point
Exact
ray location

## Slide 54: Tangential (meridional) Rays
Confined to the y-z plane.
  Object: (x, y)=(0,h)
  Pupil (xp, yp)=(0, yp), or q =0, 180
  0 ≦ r ≦1
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h

## Slide 55: Skew Rays
NOT Confined to the y-z plane.
  Object: (x,y)=(0,h)
  Pupil (xp, yp)=(xp, yp), or q ≠ 0, 180
  0 ≦ r ≦1
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h
Paraxial
Image

## Slide 56: Sagittal Rays
Skew ray with q = 90, or 270 deg.
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h

## Slide 57: Ray and wavefront, recap.
To describe aberrations, we use both of the ray error and wavefront error.
  They are related with each other (To Be Addressed).
Ray aberrations (with respect to the paraxial image point)
  Transverse ray error: (ex, ey)
    Meridional Ray
    Sagittal Ray
  Longitudinal (axial) ray error: (ez)
  Transverse and longitudinal (axial) ray error are related with each other (TBA).

## Slide 58: Transverse ray aberration : (ex, ey) On-axis object, Meridional rays
Consider an on-axis object (h=0), and meridional rays.
yp
ey
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h=0
Edge of the Pupil
+1
-1

## Slide 59: Transverse ray aberration : (ex, ey) On-axis object, Sagittal rays
Consider an on-axis object (h=0), and Sagittal rays.
xp
ex
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h=0

## Slide 60: Transverse ray aberration : (ex, ey) Off-axis object, Meridional rays
Consider an off-axis object (h ≠ 0) and meridional rays.
yp
ey
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h
+1
-1

## Slide 61: Transverse ray aberration : (ex, ey) Off-axis object, Sagittal rays
Consider an off-axis object (h=0), and Sagittal rays.
xp
ex
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h
+1
-1

## Slide 62: Longitudinal (axial) ray aberration: (ez)
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h=0
ez(yp)

## Slide 63: Longitudinal (axial) ray aberration: (ez)
Consider an on-axis object (h = 0) and meridional rays.
yp
ez
x
y
z
Xp
yp
x
y
Object plane
Pupil plane
Image plane
h=0

## Slide 64: Exact Ray Trace

## Slide 65: Wavefront aberration expansion
Fig. from E. Dreniak’s Class Note

## Slide 66: Wavefront aberration expansion
Fig. from E. Dreniak’s Class Note

## Slide 67: Seidel Monochromatic Aberration Coefficients and WFE
Spherical Aberration: W040=(1/8) SI
Coma: W131=(1/2) SII
Astigmatism: W222=(1/2) SIII
Field Curvature: W220=(1/4) SIV+(1/4) SIII
Distortion: W311=(1/2) SV

## Slide 68: Marginal Ray, Chief Ray
W. J. Smith, Modern Optical Engineering, 2nd ed.

## Slide 69: Spherical Aberration
W=
A = n i = n’ i’
h
Incoming Marginal ray
Refracted Marginal ray
u’
u
n
n’
h
R=1/c
i’
i = hc + u
Surface Normal
Paraxial Snell’s law for marginal ray
Paraxial Ray incident marginal height
Wave aberration coefficient of SA for single refractive interface
Aberration expansion of SA

## Slide 70: Spherical Aberration of a thin lens, Shape factor and conjugate factor
u’
u
R1=1/C1
R2=1/C2
n
Shape Factor
Conjugate Factor
Shape Factor : B
C=0
C=+1
C=-1
Conjugate Factor : C
Marginal Ray

## Slide 71: Spherical Aberration of a thin lens
h: incident height of marginal ray
f: power of the lens (=1/f)
Observations:
SI can be positive or negative for positive and negative powers, respectively.
SI scales (h/f)3 -> High NA lens has more SA
SI scales h4 -> W040
Important: SI is a quadratic function of B!! -> SI can be minimized for given C.
Lens Bending

## Slide 72: Minimum SA condition
Example 1: 1 to 1 imaging (magnification = -1)
C=0
B=0 : Optimum Shape is bi-convex!
Example 2: Focusing (C=-1), n= 1.5
B=0.714 : Optimum Shape is close to
Convex-Plano

## Slide 73: Minimize SA by bending for given conjugate factor
Lens bending: Vary shape factor B while keeping focal length as a constant.
By lens bending, SA can be minimized for a given conjugate factor C.

## Slide 74: Design Project #2
Singlet with minimum SA
N=1.5 (in CodeV, use 500.550 as a glass)
d-line (587.5617nm)
f=50mm,
tc=5mm
EPD 10mm
Stop at 1st surface

## Slide 75: 1st order design
Ratio of radius for the minimum SA condition
Power of the lens
Obtain R1 and R2 for f=50mm, n= 1.5

## Slide 76: Effect of Index of Refraction
Fig. from E. Dreniak’s Class Note
Higher n -> Smaller SA

## Slide 77: Effect of splitting lens
=
=
f
(f/2)+(f/2)
(f/3)+(f/3)+(f/3)
Consider splitting a singlet having a power f into 2, 3, and more lenses
while keeping the system power the same f.
= ……
Remember: the equation is an approximation. Shape factor for each element
has to be appropriately taken into account.

## Slide 78: Effect of splitting lens
Fig. from Fundamental Optical Design, M. J. Kidger
Remember: the equation is an approximation. Shape factor for each element
has to be appropriately taken into account.

## Slide 79: Design Example of Lens Splitting
Consider an optical system consisting of two positive thin lens elements having power of p1=0.01[1/mm] and p2=0.01[1/mm] (see Fig. 1). The index of refraction of the thin lens is n =1.5. Object is located at –Infinity. For simplicity, we assume zero air spacing between the thin lens elements.

## Slide 80: Procedure
Step 1: Calculate paraxial marginal ray angles, u1’, u2’. Assume the marginal ray height in the object space is 1 mm.
Step 2: Calculate conjugate factors C1 and C2 for Lens #1 and #2.
Step 3: Calculate the optimum shape factor B1 and B2.
Step 3: Based on B1, B2, and n=1.69, calculate r1,r2,r3, and r4 by using the procedure used in design project #2.

## Slide 85: Other important techniques
Negative + Positive element
Aspheric Surfaces
Concentric Surface: Marginal ray is not refracted (A=0)
Aplanatic Surface: d(u/n)=0 (To be discussed)
n
n’
n
n’
u’
u

## Slide 86: Case Study Which technique are used?

## Slide 87: Introduction to Optical Design Lecture #3
Yuzuru Takashima
College of Optical Sciences
ytakashima@optics.arizona.edu

## Slide 88: Coma

## Slide 89: Coma Function of Marginal Ray and Chief ray
Incoming Chief ray
Refracted Chief ray
q1
n
n’
R=1/c
Surface Normal
Paraxial Snell’s Law for a marginal ray
Paraxial marginal ray incident height, chief ray incident height
Paraxial Snell’s Law for a chief ray
Wave aberration of Coma at a spherical interface
Wave aberration coefficient at single spherical interface

## Slide 90: Coma Thin lens, stop at the lens
Zero-Coma condition for
Given conjugate factor C,
Example 1: 1:1 imaging system (C=0)
C=0
B=0 : Optimum Shape for zero Coma is bi-convex!
Remember: B=0 for min SA too!
Why-> Due the symmetry: Coma ~ h!

## Slide 91: Coma and SA: for C=-1 (Focusing)
n | B_zero Coma | B_min SA
1.5 | 0.87 | 0.71
2.0 | 1.67 | 1.50
2.5 | 2.57 | 2.33
B_zero_Coma ~ B_min_SA
Example 2: Focusing (C=-1)
C=-1
B=0.7~0.8 : Optimum Shape for zero Coma is close to
min SA condition too!
If we use one aspheric surface, SA can be compensated too

## Slide 92: Mini Design Project 3 Aplanatic Aspheric Singlet

## Slide 93: Design Project 3 Aplanatic Aspheric Singlet
Disk (BK7 1.2mm)
1.2mm
1.4mm
785nm
NA 0.45
f=3mm
0.05mm

## Slide 94: Specifications
Focal length : 3mm
NA: 0.45
Wave length : 785nm
Glass : Low melting temp. for glass molding (PBK40, n=1.503@785nm)
Beam diameter: 3mm
Object height: +- 0.05 mm
Wave front error < 0.02 waves in RMS
Working distance : 1.4mm
Cover glass: 1.2mm BK7

## Slide 95: Design strategy
Since the image height is small (0.05mm), we only think about SA and Coma, then we can use a single lens.
A single lens can NOT attain both zero SA and zero Coma, then we introduce two aspherical surfaces to obtain zero SA and zero Coma simultaneously.

## Slide 96: Design procedure
1st and 3rd order design
Start with minimum SA condition
Q= 0.718, R1=1.76, R2=-10.55
Optimization
Use two conic constant K of the two aspherical surfaces
Optimization using CODEV
Image evaluation
Aberration plots, Spot diagrams, Wave front error

## Slide 97: Aplanatic Surface
An optical system free of both spherical aberration and Coma is said to be Aplanatic
There is a spherical surface having zero SA and zero Coma: “an Aplanatic Surface”
The Aplanatic surface is an extremely useful in lens design, such as an oil immersion microscope, high NA lens.

## Slide 98: Aplanatic Surface

## Slide 99: Aplanatic Surface:
Aplanatic Optical System
(No SA, No Coma)
Aplanatic Surface
(No SA, No Coma)
+
Aplanatic System
(No SA, No Coma)
Surface
Normal
C
M
M’
C: center of curvature

## Slide 100: Aplanatic Surface
Given, n, n’ and L obtain r and location of final image M’ so that the surface induces no SA, Coma (and Astigmatism).
Relations
L, n’ n are known.
Location of M’

## Slide 101: Aplanatic Surface An oil immersion lens
Surface | SA | Coma | Astigmatism
Aplanatic | 0 | 0 | 0
Concentric | 0 | 0 | /=0
Aplanatic | 0 | 0 | 0

## Slide 102: Abbe’s Sine Condition
For a lens corrected for Spherical Aberration, Coma is also corrected if,
  U, U’: Exact Marginal ray angle
  u, u’: Paraxial Marginal ray angle
Special case U=0, (Object is at –Infinity)
Principal plane not a plane, but a sphere!
y

## Slide 103: Case Study: Schmidt Camera
http://www.photonics.com/EDU/Term.aspx?TermID=6884

## Slide 104: Design Project 4 Aspheric Singlet + Aplanatic surface

## Slide 105: Introduction to Optical Design Lecture #4
Yuzuru Takashima
College of Optical Sciences
ytakashima@optics.arizona.edu

## Slide 106: Astigmatism

## Slide 107: Origin of Astigmatism
I. Ogura, Modern Lens and Camera Technologies (in Japanese)

## Slide 108: Astigmatism: Surface contribution
Incoming Chief ray
Refracted Chief ray
q1
n
n’
R=1/c
Surface Normal
Paraxial marginal ray incident height
Paraxial Snell’s Law for a chief ray
Wave aberration of Astigmatism at a spherical interface
Wave aberration coefficient at single spherical interface

## Slide 109: Astigmatism Thin lens, stop at the lens
Thin lens, stop at the lens, there is not much we can do…
We have to use stop location as a design parameter.
In singlet, it is possible to compensate for astigmatism by shifting the stop. However, stop shift equation requires that Coma has to be intentionally introduced to compensate for Astigmatism.
In general, Anastigmat (SA, Coma and Astigmatism are all compensated) needs two or more lens elements and significant separation amount between the lens elements.

## Slide 110: Field Curvature
Consider imaging along the auxiliary axis. We assume Spherical aberration, Coma, and Astigmatism are compensated.
S off-axis
S’ off-axis

## Slide 111: Field Curvature
By examining the figure, and in the absence of astigmatism, the sagittal and tangential surface collapse on the a curved image surface: Petzval surface.
For a given optical system, how large is the radius of the Petzval surface?

## Slide 112: Field Curvature
Consider a single interface and imaging along the auxiliary axis.
Auxiliary Axis (Chief Ray)
c
Aperture Stop
n
n’
r
r’
r
R. Kingslake, Lens Design Fundamentals

## Slide 113: Field Curvature
By placing an small aperture at the center of curvature c, there is no Coma, no Astigmatism. Why?
Also, Spherical aberration is negligible due to the small aperture.
Under the construction, an object and image are concentric circles having
  Object distance
  Image distance
Lens law along the auxiliary axis

## Slide 114
Now consider optical system having k surfaces (k = 1, 2, 3, …)
Surface #1
Surface #2
Surface #k-1
Surface #k

## Slide 115
Take a sum over the k surfaces
Surface #1
Surface #2
Surface #k-1
Surface #k
+
+
+
+
…..
Radius of image plane
Radius of object plane

## Slide 116: Sign convention
z
z
Definition by Kingslake
Definition by CodeV
Petzval curvature is function of n & r only!!
1st order design determins Petzval curvature!!
Important!!

## Slide 117: Petzval Curvature : Examples
Example 1: Thin lens in air
z
Petzval Surface, radius r3
S1
S2
S3 (image surface)
n
r1
r2
Petzval curvature is function of
n & f only!!

## Slide 118
Example 2: Field Flattener: A negative (or positive) lens placed close to the image surface
n=1.8
n=1.5
f=100mm
f=200mm
Field Flattener
Flat field
n=1.5
Field radius ~ -100mm
Note:
produces a good design.

## Slide 119: Correction of Field Curvature
Positive + Negative power
A thick meniscus element
Field Flattener
Mirror optics (Positive power, and Positive F.C.!)
Curved detector array

## Slide 120: Field curvature and Astigmatism
Given power arrangement, shape factor, stop location, lens bending do NOT affect Petzval curvature.
However, Tangential and Sagittal surfaces change their shape in a manner such that, PT:PS=3:1, in 3rd order.

## Slide 121: Field curvature and Astigmatism
Anastigmatic lens is a lens for which Spherical aberration, Coma, Astigmatism + Field curvature are corrected.
Specifically, 3rd, 5th order Astigmatism are balanced under an appropriate amount of the field curvature.
P:Petzval
T:Tangential
S:Saggital
P
3rd
order
3rd+5th
order

## Slide 122: Seidel Aberration Coefficient of Field Curvature
Lagrange invariant
Curvature of surface
Power of thin lens
Wavefront error by Field Curvature
Wavefront aberration coefficient
Seidel coefficient (Single surface)
Seidel coefficient (Thin Lens)

## Slide 123: Distortion
Suppose, we corrected for Spherical Aberration, Coma, Astigmatism, and Field Curvature, we still have distortion of the image.

## Slide 124: Effect of Stop Location
Stop in front of the lens
Stop behind the lens
Thin Lens stop at the lens
Object (Rect Grid)
Image
?
?
?

## Slide 125: Effect of Stop Location
Stop in front of the lens
Stop behind the lens
Thin Lens stop at the lens
Object (Rect Grid)
Image
Barrel
Distortion
Pincushion
Distortion

## Slide 126: Solution: Symmetry with respect to the stop location
Object (Rect Grid)
Image

## Slide 127: Seidel Aberration Coefficient of Distortion
Lagrange invariant
Curvature of surface
Wavefront error by Field Curvature
Wavefront aberration coefficient
Seidel coefficient (Single surface)

## Slide 128: Design Project 5 (Optional) A Landscape Lens