## Slide 1: OPTI/ASTR 528 Lecture 9
Atmospheric turbulence: effects on the image
(What happened to the light on the way to my focal plane???)
Michael Hart
Feb 12, 2015

## Slide 2: Outline
A (very) quick review of Fourier optics
The point-spread function
OPD errors and turbulence really messing things up
Characterizing the turbulence statistically: seeing, anisoplanatism, spatial, temporal and angular scales

## Slide 3: Fraunhofer diffraction
Fraunhofer diffraction describes the ‘far-field’ behavior of the field, i.e. what it looks like after travelling essentially infinite distance. (N.B. ‘Infinite’ is to be understood in terms of the wavelength)
where k=2p/l.
(Primed quantities are in the aperture plane; unprimed in the image plane.)
Credit: Wikipedia
Aperture
plane
Image
plane

## Slide 4: Fraunhofer diffraction
With fx = x/lz and fy = y/lz the equation becomes
which we recognize as the Fourier transform of the aperture function U’

## Slide 5: The point-spread function (PSF)
The PSF is the irradiance distribution in the focal plane when it’s looking at a point source.
  Strictly, it’s a mathematical construct only, since there’s no such thing as a genuinely point-like source. It wouldn’t emit any light. But an image of an unresolved source is a very good approximation to the PSF. Even if the unresolved source is, say, 107 meters across (a large star – provided it’s far enough away).
But irradiance is proportional to the square of the electric field’s amplitude. It’s what an optical imaging sensor actually detects. So, if U(x’,y’,0) is a plane wave entering our optical system, then the PSF P(x,y) is
In words: the PSF is the power spectrum of the electric field in the aperture of the imaging system.

## Slide 6: Incoherent imaging
If I image a collection of point sources in the field of view, each one will make a little copy of the PSF of corresponding brightness.
Assuming the sources are not coherent (with each other), the irradiances will simply add to give my final image.
One ‘star’…
…two ‘stars’…
…three ‘stars’
Source brightness at field point (x’,y’)
PSF
Image irradiance at field point (x,y)

## Slide 7: Incoherent imaging
If, instead of a bunch of discrete point (like) sources, the scene is a continuous distribution of non-zero brightness, then the sum over the field becomes an integral:
And that is just the convolution of the scene radiance B with the PSF P.
We can write this very conveniently in the Fourier domain as
where . is called the Optical Transfer Function (OTF)
Because of this convenient truth, and the nature of an imaging system’s effect on light passing through it, you’ll find that an AO simulation code spends much of its time doing Fourier transforms.

## Slide 8: ‘Perfect’ PSF for a circular aperture
Most of the imaging systems you’ll run across have circular apertures (why is this?)
PSF for a circular aperture is just the power spectrum of a disk. It has the form:
where J1 is the first-order Bessel function of the first kind. This works when the units of all lengths are in meters.
l = wavelength
D = aperture diameter
f = system focal length
r = radial position in focal plane
FWHM = 1.029 l/D

## Slide 9: ‘Perfect’ PSF for a 2-beam aperture (e.g. LBT)
A qualitative assessment:
In this case, the PSF looks like the PSF for the individual circular segments multiplied by a cosine wave whose frequency is inversely proportional to the segment separation.
FWHM = l/B
Pupil geometry
B

## Slide 10: ‘Perfect’ PSF for a 2-beam aperture (e.g. LBT)
A quantitative assessment:
W1 and W2 are window functions that define the segments of the pupil.
Q(x,y) has a particular physical interpretation: it’s the optical path difference between the two apertures to a point (x,y) in the focal plane.
B
W1
W2
PSF of aperture 1
PSF of aperture 2
Coherent cross term
(this is what makes the fringes)

## Slide 11: Phase effects on the PSF
With Q=0, there’s a central bright fringe.
BUT – if we introduce a non-zero OPD d into the path from one of the two apertures, the fringes shift by a fractional amount D:
Real star images from the LBTI!
The Large Binocular Telescope on Mt. Graham, AZ

## Slide 12: Now, add more segments…
Six-fold symmetry of the aperture is apparent in the PSF.
It’s almost starting to look like the PSF from a filled aperture, with a central lobe surrounded by rings, where the effective aperture size is the circumscribing circle around the entire 7-segment array – 25 m!
Every pair of mirror segments generates a set of fringes, just like LBT.
There are 21 segment pairings: i.e. 21 sets of cosine fringes that all multiply together coherently.
Giant Magellan Telescope
Simulated PSF

## Slide 13: Effect of OPD errors
When random OPD errors are introduced between the 7 segments, the 21 sets of fringes all move, just like the LBTI fringes.
The (now perturbed) PSF has become a set of ‘speckles’.
  Each retains the size of the central lobe of the pristine PSF because it’s still made by constructive interference from overlapping sets of fringes that have a period determined by the primary mirror segment spacing.
  The bright/dark distribution of each fringe set has been moved away from the optical axis by the corresponding OPD error, so energy shows up in places other than the center of the PSF.
No OPD errors
Random OPD errors between segments

## Slide 14: Analogy with turbulence-induced OPD errors
The atmospheric refractive index fluctuations impose OPD errors between segments – and they have just this effect on the PSF (breaking it into diffraction-limited-size speckles)
That’s what caused the fringe wander in the LBTI star movie earlier.
GMT is (well, will be…) close to a filled aperture, but we can also think of a real filled aperture as being conceptually filled with segments that have dynamically evolving OPD errors between them introduced by the atmosphere.
We can expect, then, that the instantaneous (and monochromatic) PSF of a filled aperture telescope looking through atmospheric turbulence will have the same character of being broken up into speckles, each at about the size of the diffraction limit l/D.
What remains (coming shortly!) is to define how big these conceptual ‘segments’ are, and how many speckles they create in the PSF.

## Slide 15: Fourier components and speckles (amplitude)
Imagine I put a transmission mask over my imaging system’s aperture that looks like a sine wave (i.e. a single Fourier component), with n cycles per aperture
  Field in the aperture is then sin(2pnx’/D)+1
  No such thing as negative transmission, so we can’t make the amplitude be strictly just a single Fourier component!
The field in the focal plane will be:
Then the PSF will be:
So we should see one speckle on axis, and one each at x = nlz/D that are ¼ as bright

## Slide 16: Fourier components and speckles (amplitude)
And that is just what we do see! A result that will be familiar to anyone who’s worked with transmission gratings.
Amplitude
Phase
PSF
4l/D
n = 4

## Slide 17: Fourier components and speckles (phase)
Now let’s say I replace the transmission mask with a sinusoidal phase mask at the same spatial frequency (Aha! I can have negative phase values!) We’re using a phase grating.
  Field is now A sin(2pnx’/D), where A is a constant amplitude
This is a little trickier, but the PSF comprises an infinite series of speckles spaced by nl/D (in angle).
Amplitude
Phase
PSF

## Slide 18: Fourier components and speckles
So, can we just look at where the speckles are, how bright they are, and figure out the wavefront aberration one Fourier component at a time??
Sadly, no.
What can’t we tell about the field?
Amplitude
Phase
PSF

## Slide 19: Simulated atmospheric PSFs (with real light)
This video was made with an atmospheric simulator in lab 553 in Steward Observatory last week. The simulator’s designed as a test tool for AO systems that we’re building now.
Two acrylic plates have been machined with specific realizations of Kolmogorov turbulence. They’re mounted in rotating bearings so they can be inserted into a light beam and turned (at different speeds, in different directions) to mimic the behavior of an atmosphere with two layers of turbulent aberration.
Speckles!

## Slide 20: Critical parameters of the aberration
The analogy to a segmented pupil with OPD errors is a good one, but we need to know more: how can we characterize the size of the atmospheric ‘segments’ in our filled-aperture pupil? How fast does the speckle structure evolve?
And one other thing we haven’t touched on yet: how does the speckle structure change as we look along different lines of sight?
Short digression to introduce anisoplanatism…

## Slide 21: Anisoplanatism
Phase aberration introduced near the pupil is common to the entire scene.
Aberration further away is seen differently at different points in the scene and is the source of what’s called anisoplanatism.
The PSF (including the effects of the atmosphere) is not shift invariant! Not by a long way.
The angle over which the PSF is more or less constant is called the ‘isoplanatic angle’. It’s a function of wavelength and the atmospheric Cn2 profile.
We’ll quantify ‘more or less’ a little later.
Common boundary-layer turbulence
Distant turbulence
Objects in the scene
Telescope
Image of the scene

## Slide 22: Critical parameters of the aberration
OK, back again…
We care about spatial, temporal, and angular scales of the aberration.
  We’ll be assuming that everything descends from turbulent flow that obeys Kolmogorov statistics. In reality, one sees variations from this all the time because other effects (like local topography) interfere with the requirement that the energy cascade happen in an unconstrained fluid.
Because the power spectrum and structure function of the aberration obey power laws, as we saw earlier from John, we can expect that each of these scales will be characterized by a single parameter.
They are, respectively:
r0 Atmospheric coherence length
t0 Atmospheric coherence time
q0 Isoplanatic angle
  Of course, the power law behavior doesn’t extend over all scales (just the inertial subrange), so there will be some limits to the application of these parameters, but as we’ll see, they’re very useful over scales we care about (telescope sizes and fields of view, and AO correction times).

## Slide 23: So, what does Kolmogorov phase aberration actually LOOK like?
Simulation of a Kolmogorov wavefront
There are variations going on at all spatial scales here – as expected (see the structure function plot below left)
There is indeed only one parameter to quantify: the vertical position of the structure function, which will tell us how strong the turbulence is.

## Slide 24: r0, the Fried scale (revisited)
A practical way to quantify the strength of the aberration: define how big a telescope can be before the aberrations get to be so bad that it’s PSF is no longer diffraction limited.
  Note that this will also be the size of the ‘segment’ in our description of
In Lecture 7, we had the derivation of the phase structure function in terms of r0
And since also
We can write
This is one of the crucial equations to know when designing AO systems!

## Slide 25: Dependence of r0
r0 depends on:
  Wavelength, as l6/5. It gets better (larger) as the wavelength increases. That means, for example, a 1 m telescope will not be diffraction limited in visible light (r0 ~ 15 cm), but will be in the infrared at 2.5 mm (r0 ~ 92 cm).
  Zenith angle, as (sec z)-3/5. r0 gets worse (smaller) as a telescope looks further away from zenith – i.e. looks through more turbulent atmosphere.
Cn2 profile measured with SCIDAR at Mt. Graham
Credit: Elena Masciadri
  The Cn2 profile. After all, it’s the strength of turbulence that we’re trying to quantify with r0!

## Slide 26: r0 and speckle structure
If r0 defines the largest patch of wavefront that I can image at the diffraction limit, then it also naturally defines the size of a segment within a filled aperture that I can consider to have a common OPD (which is why it’s commonly called the coherence length)
So how many r0 sized patches are there in the aperture of a telescope of diameter D?
  Well, ah, (D/r0)2 of course
That creates ~ ½ (D/r0)4 sets of ‘fringes’ in the focal plane
BUT, about (D/r0)2 sets of fringes are redundant (that is, different pairs of r0 sized patches will, by chance, have about the same separation and orientation – meaning the fringes they create are not distinct)
So, finally, we conclude that a short-exposure image of a point source will comprise ~ (D/r0)2 speckles.

## Slide 27: r0 and telescope resolution
Again, r0 defines the largest telescope that will make a diffraction limited image.
Averaged over time, as speckles wash out, resolution of a large telescope is reduced to l/r0, the same as it would be if it had diameter r0
D/r0 = 2
D/r0 = 4
D/r0 = 8
These simulations used the same aberrations, just scaled differently.
  General distribution of energy is similar
  Overall energy spread is ~ l/r0, with l/D speckle size

## Slide 28: Typical values of r0 and seeing
Good site (e.g. Mt. Graham, Bad site (e.g. Albuquerque)
Mauna Kea)
(mm) r0 (m) r0 (m)
0.50 0.2 0.05
0.75 0.33 0.08
1.0 0.46 0.12
2.5 1.38 0.35
5.0 3.17 0.79
10.0 7.28 1.82
Astronomical “seeing” is defined as the FWHM of the long-exposure PSF, i.e. seeing = l/r0. It is almost always quoted at an industry-standard wavelength of 0.5 mm.

## Slide 29: Temporal coherence
Next time:
How fast does the PSF evolve (i.e. how fast does our AO system have to work to keep up)?
How big is our corrected field of view? And can we do anything to make it better? (Well, yes, or I wouldn’t be asking.)