## Slide 1: OPTI340 Lens Design Lecture #1
Yuzuru Takashima
College of Optical Sciences
ytakashima@optics.arizona.edu

## Slide 2: Design Procedure
1) Statement of problem to be solved:
  Objective
  Technical statement (PRD: Product Requirement Document)
  Marketing statement (MRD: Marketing Requirement Document), which translates into a technical statement
2) Alternative designs:
  Several options for solving the stated problem/objective
3) First order designs: geometrical design of optics
4) Evaluate against objectives
5) Select the most promising solution(s) (1st order. solution)
6) Carry out ray tracing design of most promising first order design
7) Evaluate design against objectives; optimize against “cost” factor
8) Go through loop 6, 7, 6, 7 until satisfactory results emerge, or 3, 4, 5, 6, 7
9) Carry out tolerance analysis, manufacturing and cost analysis, repeat 3-8 if necessary
10) Write report

## Slide 3
1. Statement of problem to be solved:
Objective
Marketing and Technical statement
5. Select most promising solution(s)
(1st order solution)
2. Alternative designs:
Several options for solving the stated problem/objective
3. First order designs:
8. Carry out ray tracing design of most promising 1st order design
9. Carry out tolerance analysis, manufacturing and cost analysis
4. Evaluate
against objectives
7. Evaluate
against objectives
10. Evaluate
against objectives
Yes
No
Yes
No
6. Carry out 3rd order analysis
(3rd order solution)
1) Statement of problem to be solved:
  Objective
  Technical statement (PRD: Product Requirement Document)
  Marketing statement (MRD: Marketing Requirement Document), which translates into a technical statement
2) Alternative designs:
  Several options for solving the stated problem/objective
3) First order designs: geometrical design of optics
4) Evaluate against objectives
5) Select the most promising solution(s) (1st order. solution)
6) Carry out ray tracing design of most promising first order design
7) Evaluate design against objectives; optimize against “cost” factor
8) Go through loop 6, 7, 6, 7 until satisfactory results emerge, or 3, 4, 5, 6, 7
9) Carry out tolerance analysis, manufacturing and cost analysis, repeat 3-8 if necessary
10) Write report
Design Procedure

## Slide 4: Waterfall v.s. Agile Process
Waterfall process
  Mainly used for a hardware design.
  It is very important to follow the process!
    A self-reviewing process
    Logical development
    Easy to recover errors

## Slide 5: Agile Process
Agile Process
  For software development, it is generally difficult to define PRD completely.
    Look & Feel
    User experience.
Specification
MRD
PRD
Testing

## Slide 6: Example: 1) Statement of problem to be solved
  Marketing statement:
    I want to focus (and scan) a laser beam on a sample inside a vacuum chamber. Size of the chamber is 80mm in diameter.
  Technical statement:
    Focal length of 40mm is required, i.e. from requirements for scanning speed.
    Wavelength:
    Spot size:
    f’=40mm.
    Working distance (=fb) > 45mm.
    Less number of elements is desirable for alignment.
    Anything else?
80mm
Optical
System
Laser
Sample
Chamber
45mm
Scanning
mirror

## Slide 7: 2) Alternative designs 3) First order designs: geometrical design of optics
Single thin lens
f’=40mm
Thick lens
(01LDX313,f=40mm)
H
H’
f’=40
fb=39
Two thin element system
f’sys=40, fb = 80
f’=-40
f’=+40
40
Ray matrix
Graphical ray tracing
40
40
n
Thick lens
01LDX313
f=40mm
Thick lens
01LDK117
f=-40mm
F’sys
F’sys
F’sys
40 n
79
80
H H’
H H’
Single thick lens
Single thick lens
Two thick lenses
Start!
F’sys
F’sys
f’=40

## Slide 8: 4) Evaluate against objectives 5) Select most promising solution (1st order. solution)
H
H’
f’=40
fb=39
40
n
F’sys
F’sys
40 n
79
80
H H’
H H’
1) Single thick lens
2) Single thick lens
3) Two thick lenses
F’sys
 | 1) Single thick lens | 2) Single thick lens | 3) Two thick lenses
1. l=532nm | 532 | 532 | 532
2. f’sys =40mm | 40 | 40 | 40
3. fb>45mm | 39 (< 45) | 80 | 79
4. # of elements | 1 | 1 | 2
5. Spot size<10mm | 2.44l(F/#)=4.15mm, (F/#)=3.2 | Need further evaluation by ray tracing (Step 6 and thereafter.) Note: too thick! (~60mm) | 2.44l(F/#)=8.3mm, (F/#)=6.4 Need further evaluation by ray tracing (Step 6 and thereafter.)